## Slide 1
Solidwork Files
Assembly 9978 is IP region.
Assembly file above that is for entire beamline.

## Slide 2: Run Plans
Target smaller spotsize on IP
  Tune with photohybrid correctors
Quadscans on screen5
Take data showing linac tuning with beam on beamdump
Propagate beam through pinhole
Charge confirmation, transmission to IP.
Jitter measurements of beam

## Slide 3: To do list
Hall probe interlock
Rearrange power supplies.
Dipole power supply
Alignment laser

## Slide 4: Installation
Popins
  Air connections, PLC controls/cables
Cameras
  Lenses
  Power cables
  Ethernet
Steering magnets
  Power supplies

## Slide 5: Friday, 8/9/24
Changed gun temps back to nominal values
  Chiller1: 30 C
  Chiller2: 27.5 C
  Chiller3: 26.5 C
Alignment between IP and Cam5
  Very different. Beam found on dump with nearly 0 A on steering 4.
  Can we move laser/pinhole to match ebeam axis?
Gun and Quad scan

## Slide 6: Gunphase scan
Charge and pixel sum
  Why the “shift”. Revisit when second ICT on beamline.
We were operating at 268 degrees.
  Towards the compression point.
Chart: Gunphase Scan

## Slide 7: Tuesday, 8/13/24
Found beam on beam dump
  146 Amps corresponds to 93 MeV
Limited in steering. Revisit after installation