## Slide 1: BELLS Update
8/15/2024

## Slide 2: Photohybrid
Increased Charge
  Reduced losses on UV transport
Well-defined operating phase
Chart: Gunphase Scan

## Slide 3: Linac Structures
Beam alignment and tuning
  Similar settings day to day
  Fast procedure (~30 min)
Structure tuning
  Adjust phase/frequency to maximize energy
  Coarse: deflection from steering magnet
  Fine: dump dipole current
Steering 1
Steering 2
Steering 3

## Slide 4: Beam Focusing
60 um spotsize at interaction point (IP)
  7 um/pixel calibration
  Tune with photohybrid correctors
Screen Alignment
  Motorized IP screen
  Alignment laser (long term benefits)

## Slide 5: Quad Scan Measurement
Quad Scan
  Save spotsizes at various focusing
  Optimize beam matrix to minimize error between simulation and data
Reveals beam emittance
  mm*mrad
  Tunable figure of merit
Use simulation as guide
  Matrix model in Elegant and Python
  Initial beam matrix from optimization
Triplet IP Doublet Dump
Start
(Linac exit)
Weak focusing
Strong focusing

## Slide 6: Data Collection
Saving images and beamline settings
  Image statistics, charge, steering, quads, etc
  Manual measurements
Utilize scripts to automate measurements
  Quad scan, steering raster scans
  Faster, repeatable
ROI
Gaussian Fit

## Slide 7: Beam Dump
Beam found at 146 Amps on dipole
  Corresponds to ~90 MeV
Correctly manipulated by dipole and quads
  Adding steering
Align after beamline upgrades
  Fix dump to floor

## Slide 8: Current Beamline
Stripline BPM
Replace with YAG or OTR
Button BPM
Replace with ICT
Button BPM
Replace with Stripline BPM
Ion Pump on Tee
Replace Tee with Cross and add OTR, Move after Doublet

## Slide 9: Proposed Solution
Custom Length 6-way CF Cross
Modified G-11W-150 (in stock)
2.75” CF Cube
Ion Pump moved here
OTR Added
Stripline BPM
Remove Button BPM
ICT
Add 4.5” to 2.75” ZLR & Custom Adapter to 6” Cube, Studs needed
Install Comments:
Two steering magnets in hand
One pair of power supplies
  Nathan ordered more
YAG after IP for pinhole alignment.

## Slide 10: Alignment Laser

## Slide 11: IR Laser Status

## Slide 12: RF Status

## Slide 13: Next Steps
Install steering and diagnostics (ICT and screens)
Optimize structures with dump dipole
Transport electron beam through pinhole
Run for light