## Slide 1: Summary of GRIT Runs

## Slide 2
Solidwork Files
Assembly 9978 is IP region.
Assembly file above that is for entire beamline.

## Slide 3: Beamline To do
Camera field of view
Logistics for installation
  Popins
    Enough air hoses
  Cameras
    Lenses
    Power cables
    Ethernet
Cameras slide for Marcos

## Slide 4: Friday, 8/9/24
Changed gun temps back to nominal values
  Chiller1: 30 C
  Chiller2: 27.5 C
  Chiller3: 26.5 C
Checked alignment on IP and Cam5
Gun and Quad scan

## Slide 5: Gunphase scan
Scaled pixel sum (subtract minimum)
Redo with laser off.
We were operating at 268 degrees.
  Ask Maksim about how charge scan was measured.
Chart: Gunphase Scan

## Slide 6: Quad Scans
Created simple matrix model in Python.
  Checked against elegant simulation
Given quad currents and spotsizes, optimize beam matrix to minimize error between simulation and data
  Estimates emittance
  Gives input twiss parameters for elegant simulation

## Slide 7: Cameras
 | Cam1 | Cam2 | Cam3 | IP | Cam5 | Beam Dump | Extra | Extra
Screen | 1” yag | 1” yag | ½” OTR | ½” OTR | ½ OTR | 1” yag |  | 
Visible Aperture | 18mm | 18mm | 9mm | 9mm | 9mm | 18mm |  | 
Flip LR? | True | True | False | False | True | True |  | 
Flip TB? | False | False | True | False | False | False |  | 
See GRIT Operations/Calibrations/Cameras