## Slide 1
8/16/2024
GRIT Monthly
Prepared by
RadiaBeam Technologies, LLC.
GRIT DARPA BAA Contract # HR001120C0072
and SBIR Awards # W912CG22C0032, W912CG22C0033

## Slide 2: Topics to be Covered
Runtime Optimization (Andrew Fisher)
Diagnostic Upgrade
Laser Status
Next Steps

## Slide 3: Photohybrid
Increased Charge
  Reduced losses on UV transport
  Adding second ICT after structures
Well-defined operating phase
Chart: Gunphase Scan

## Slide 4: Linac Structures
Beam alignment and tuning
  Similar settings day to day
  Fast alignment procedure
Structure tuning
  Adjust phase/frequency to maximize energy
  Coarse: deflection from steering magnet
  Fine: dump dipole current
Steering 1
Steering 2
Steering 3

## Slide 5: Beam Focusing
50 um rms spotsize at interaction point (IP)
  7 um/pixel calibration
  Targeting 10 um
  Tune with photohybrid correctors
Screen Alignment
  Motorized IP screen
  Alignment laser (long term benefits)

## Slide 6: Quad Scan Measurement
Quad Scan
  Save spotsizes at various focusing
  Optimize beam matrix to minimize error between simulation and data
Use simulation as guide
  Matrix model in Elegant and Python
  Initial beam matrix from optimization
Quads will be operated up to 10A.
Triplet IP Doublet Dump
Start
(Linac exit)
Weak focusing
Strong focusing

## Slide 7: Data Collection
Saving images and beamline settings
  Image statistics, charge, steering, quads, etc.
  Manual measurements
Utilize scripts to automate measurements
  Quad scan, steering raster scans
  Faster, repeatable
ROI
Gaussian Fit

## Slide 8: Beam Dump
Beam found at 146 amps on dipole
  Corresponds to ~90 MeV
Correctly manipulated by dipole and quads
  Adding steering
Align after beamline upgrades
  Fix dump to floor
Energy Axis

## Slide 9: Current Beamline
Stripline BPM
Replace with 1” OTR
Button BPM
Replace with ICT
Button BPM
Replace with Stripline BPM
Ion Pump
Replace Tee with cube and 1/2” OTR, Move after Doublet
6”x4.5” ZLR
Remove and replace with 6”x2.75” ZLR from upstream
6”x2.75” ZLR
Remove and move to downstream ZLR position
½” YAG
Remove YAG (use OTR), Move to before Dump Dipole
Replace with new 1” YAG ASM

## Slide 10: Proposed Solution
1” OTR
Custom cross from previous emittance slit assembly
2.75” CF Cube, ½” OTR
Ion Pump moved here, ½” Setup Moved from after Dump Dipole
Stripline BPM
Taken from upstream, Remove Button BPM
ICT
Add 4.5” to 2.75” ZLR, Metric Studs
2.75” CF Nipple
13.85” Long
2.75” CF Nipple
18.25” Long
4.5”x6” Adapter
2” Long, Metric Studs
2.75” CF Cube, 1” YAG
New Assembly
Add YAG screen
½” OTR becomes ½” YAG

## Slide 11: Reference axis laser
Diode laser input
Top view of the accelerator
Experiments have shown we were missing the accelerator’s axis position
We are installing a diode laser at the most upstream camera position
Using the back of the mirror used to visualize the cathode
Propagating the diode laser down the most downstream OTR
Diode output on
new OTR camera

## Slide 12: IR laser
After recent AC shut down and constant accelerator’s operation, laser work on IR was limited
The UV beamline and IR beamline setup from Amplitude has been modified so their alignment can be tuned individually
We re-aligned the laser in the cleanroom after the AC shutdown and propagated it to the bunker
Currently propagating the IP to propagate IR laser through the IP pinhole during shutdown

## Slide 13: Next Steps
Install steering and diagnostics (ICT and screens)
Fine tune structures with dump dipole
Optimize spotsize and transport through pinhole
Run for light